## Slide 1: EEC 130A Introductory Electromagnetics I
Lecture 14
Winter 2012
Dr. Xiaoguang “Leo” Liu
Electrical and Computer Engineering
UC Davis

## Slide 2: What to do after 130A?
Courses
  130B, taught by Prof. Branner next quarter
  132ABC: RF / Microwave circuits
  133: Principles and applications of antenna
A few options if you are interested in RF/Microwave Engineering
http://rfengineer.net/1511/radio-architectures-pt-5-adcs-and-receivers/

## Slide 3: Courses
289N: RF-MEMS and Adaptive Wireless Communication Systems
  Radio Frequency Micro-Elelctromechanical Systems
Radant MEMS Switch
Thick cantilever
Signal
Signal
ON State (contact)
Bias Electrode
OFF State (no contact)

## Slide 4: Why RF-MEMS?
So, can’t you do this with transistors? After all they are …
Yes, but…
They are non-linear devices (semiconductor junctions)
Constant biasing current in the on state
They have quite high loss for high frequencies (several GHz)
They leak in the off state at high frequencies
Really small (~nm)
Really fast (~100ps)
CAUTION = may be much larger for RF

## Slide 5: Why RF-MEMS
Low loss (0.1 dB up to 120 GHz)
Low power consumption (µW for electrostatic actuation)
High Isolation (> 30 dB up to 100 GHz)
High linearity (Very low intermodulationproducts > 60 dBm)
Very high Q possible with varactors(and large capacitance range)
Potential for low cost fabrication (no epilayers, no 0.15 um litho.)
RF-MEMS switches are:

## Slide 6: Applications of RF-MEMS
Cellphone “Death Grip” problems

## Slide 7: RF-MEMS Comes to the Rescue
RF-MEMS based antenna impedance tuner

## Slide 8: 289N RF-MEMS
A general introduction on the modeling, design, fabrication, and characterization of RF-MEMS
Prerequisite: 130A & B
Expected outcome:
  Understand the advantages and limitations of RF-MEMS technology
  Understand the working principles of the state-of-the-art RF-MEMS devices
  Evaluate the merits and drawbacks of an RF-MEMS design
  Quickly read and understand a paper on RF-MEMS and judge its quality
  Complete a design of an RF-MEMS device or circuit with the help of CAD packages
  Deliver a report and a presentation on a topic in RF-MEMS

## Slide 9: Projects for Fun
Smith chart iPhone app
Building a HAM radio and getting a license
Sucks
$14.99
NorCal 40A
Come Up with
Your Own Idea

## Slide 10: Senior Design
Senior design project in RF/Microwave systems
  Department requires at least 3 students to form a team
  Some examples from other schools:
Purdue: Microwave
Powered Helicopter
TAMU: Phase Based
RF Direction Tracking

## Slide 11: Senior Design
Some more ideas (from the almighty Internet)
  Vertical Navigation Radar (http://lea.hamradio.si/~s53mv/vnr/assembly.html)
  Microwave Handy Scanner (http://www.youtube.com/watch?v=vDyo_OQFdAc)
  Speed Radar (http://www.youtube.com/watch?v=Dhp21FxttWM)

## Slide 12: Review
Magnetostatics
Magnetic force & torque

## Slide 13: Review
Biot-Savart Law

## Slide 14: Maxwell’s Magnetostatic Equations
Gauss’s Law for Magnetism
There is no magnetic charge (or magnetic monopole)

## Slide 15: Ampere’s Law

## Slide 16: Example: Internal Magnetic Field
For r < a

## Slide 17: Example: Internal Magnetic Field
For r > a

## Slide 18: Magnetic Field of Toroid
Applying Ampere’s law over contour C
The magnetic field outside the toroid is zero. Why?
Ampere’s law states that the line integral of H around a closed contour C is equal to the current traversing the surface bounded by the contour.